## Slide 2
Safety Threats
(accidental origin)
Cyber Security threats
(Malicious intention)
UAS operation out of control
Harms
Issue de Safety
Issue de Sécurité
SORA
OSOs(*)
OCSOs (**)
(*) OSO: Operational Safety Objective
(**)OCSO: Operational Cyber Security Objective
New
component
Resume of the extention of bow-tie model

## Slide 3
Open category
(Low risk)
Specific category
(Medium risk)
Certified category
(High risk)

## Slide 4
Threats
Hazard
(UAS operation out of control)
Fatal injuries to 3e parties on ground
SORA
OSO
New
component
Fatal injuries to 3e parties in air
Digital damage to infrastructure
Extended bow-tie model bow-tie model with new harm category

## Slide 5
Likelihood of fatal injuries to 3e parties on ground
Likelihood of having UAS operation out of control
(1)
Likelihood of person struck by the UA if the operation is out of control
(2)
Likelihood that, if struck, person is killed
(3)
=
x
x
Likelihood of fatal injuries to 3e parties in air
Likelihood of having UAS operation out of control
(1)
Likelihood of other A/C struck by the UA if the operation is out of control
(2)
Likelihood that, if struck, the other A/C cannot continue a safe flight and landing
(3)
=
x
x
Likelihood of digital damage to the Digital infrastructure
Likelihood of having UAS operation out of control
Likelihood of digital security violation if the operation is out of control
Likelihood that, if a successful violation,
the digital infrastructure is damaged
=
x
x
Likelihood of privacy invasion for 3e parties
Likelihood of having UAS operation out of control
(1)
Likelihood of person exposed to UA if the operation is out of control
(2)
Likelihood that, if exposed, privacy of person is violated
(3)
=
x
x
Notes: Pour vous expliquer les processus de SORA. Je vais commercer par la approche qualitative de SORA.
Je vous rappelle: l’objective est de détérminer des OSO pour que les likelihood de 2 harm soit acceptable.

## Slide 6
VERY HIGH |  |  |  | 
HIGH |  |  |  | 
MEDIUM |  |  |  | 
LOW |  |  |  | 
SEVERITY LIKELIHOOD | LOW | MEIDUM | HIGH | VERY HIGH
ACCEPTABLE
NON - ACCEPTABLE
Risk evaluation table

## Slide 7
UAS operation out of control
Technical issues
Human errors
Adverse operating condition
Deterioration of external systems supporting UAS
Fatal injures to third parties on ground
Fatal injure to third party in air
OSOs
Harm barriers
Attack on communication
Attack on Software
Attack on Sensors
OCSOs
Extended model with new CS threats

## Slide 8
CONOPS
description
GRC determination
Ground risk > 7 ?
ARC determination
OSO robustness determination
Operation modification
No
Input for system design
Yes
SAIL Level determination
Resume of the extention of bow-tie model

## Slide 9
CONOPS
description
GRC determination
Ground risk > 7 ?
ARC determination
SAIL Level determination
(Module 2)
OSO robustness determination
Operation modification
No
Input for system design
OCSO robustness determination
(Module 1)
DIRC determination
(module 2)
Yes
CSC Determination
(Module 1)
Integrated process

## Slide 10
CONOPS
description
GRC determination
Ground risk > 7 ?
ARC determination
SAIL Level determination
(Module 1)
Operation modification
No
DIRC determination
(Module 1)
Yes
Proposed Eextended workflow in module 2

## Slide 11
CONOPS
description
GRC determination
Ground risk > 7 ?
ARC determination
SAIL Level determination
(Module 1)
Operation modification
No
PRC
determination
(Module 1)
Yes
Proposed Eextended workflow in module 2

## Slide 12
Proposed Eextended workflow in module 2
CONOPS
description
GRC determination
Ground risk > 7 ?
ARC determination
SAIL Level determination
(Module 1)
Operation modification
No
PRC
determination
(Module 1)
Yes

## Slide 13
CONOPS
description
GRC determination
Ground risk > 7 ?
ARC determination
SAIL Level determination
(Extension 1)
Operation modification
No
PRC determination
(Extension 1)
Yes

## Slide 14
SAIL Level determination
OSO robustness determination
Input for system design
OCSO robustness determination
(Module 1)
CSC Determination
(Module 1)
Proposed Eextended workflow in module 1

## Slide 15
3. Spirit of assessment method in quantitative approach
a. Likelihood of « Fatal injuries to 3e parties on ground »
Likelihood of digital damage to the Digital infrastructure
Likelihood of having UAS operation out of control
Likelihood of digital damage digital infrastructure if UAS operation out of control
=
x
Notes: Pour vous expliquer les processus de SORA. Je vais commercer par la approche qualitative de SORA.
Je vous rappelle: l’objective est de détérminer des OSO pour que les likelihood de 2 harm soit acceptable.

## Slide 16
Extended model with new CS threats
UAS operation out of control
Technical issues
Human errors
Adverse operating condition
Deterioration of external systems supporting UAS
Fatal injures to third parties on ground
Fatal injure to third party in air
OSOs
OSOs
OSOs
OSOs

## Slide 17
UAS operation out of control
Technical issues
Human errors
Adverse operating condition
Deterioration of external systems supporting UAS
Fatal injures to third parties on ground
Fatal injure to third party in air
Threat
Hazard
Harm

## Slide 18: Résumé du sujet de discussion
2. Les modules d’extensions de SORA ver Cyber-Security (CS)
Technical issue with UAS
Deterioriation of external supporting system
Human error
Aircraft in collision course
UAS operation out of control
Fatal injuries to 3e party on ground
Fatal injuries to 3e party in air
OSO
OSO
OSO
OSO
Harm barrier(s)
Adverse weather condition
OSO
Cyber-security threat
OCSO
Module 2
Fatal digital damage to the Digital Infrastructure
Module 1
Notes: Tout d’abord, je vous rappelle 2 défintions importantes utilisé par SORA.
+ Risque, comme tous les norme dans domain aéronautique, risque d’un occurrence est un variant de 2 dimensions contient likelihood et severity de cette occurent
+ 2e définition, c’est modèle bow-tie ou nœud papillon. C’est un graphique utilisé pour représenter les scénarios qui peuvent arriver. Chaque scénario contient 3 occurrences: threat, hazard and harm. Threat entraine Hazard, Hazard entraine harm. Il y a aussi 2 petite bloque Threat barrier et Harm barrier qui représente les contre-mesure: threat barrier diminue likelihood de threat/hazard, Harm barrier diminue likelihodd de harm.

## Slide 19
Extended model with new CS threats
UAS operation out of control
Technical issues
Human errors
Adverse operating condition
Deterioration of external systems supporting UAS
Fatal injures to third parties on ground
Fatal injure to third party in air
Cyber security threats
Damages to Infrastructure and Privacy violation
Module 2
Module 1
OCSOs
OSOs
Threat side
Harm side
Harm barriers

## Slide 20
Extended model with new CS threats
UAS operation out of control
Technical issues
Human errors
Adverse operating condition
Deterioration of external systems supporting UAS
Fatal injures to third parties on ground
Fatal injure to third party in air
Cyber security threats
Damages to Infrastructure and Privacy violation
Extension 2
Extension 1
Threat
Harm

## Slide 21
Equation to calculating pixel density
PD = (pixel/m)
ϕ
h
h (m): altitude of drone
ϕ : angel of view of camera

## Slide 22: Extend the method SORA for privacy consequences
(b) How to evaluate Privacy Risk Class (PRC) of a given UAS operation?
Determine PRC
Type of operation | Unpopulated zone, VLOS | Unpopulated zone, BLOS | Populated zone, VLOS | Populated zone, BLOS
Level of detail of image |  |  |  | 
Monitor | A | B | C | D
Detect (>25 pixels/m) | B | B | 1 | 1
Observe (>62.5 pixels/m) | C | 1 | 1 | 1
Recognize (>125 pixels/m) | D | 1 | 1 | 2
Identity (>250 pixels/m) | E | 1 | 2 | 2
Inspect (>1000 pixels/m) | 1 | 2 | 2 | 2